## Slide 1: A Rapid Compression Study of the Butanol Isomers at Elevated Pressure
Bryan Weber and Chih-Jen Sung
Prepared for
7th US National Technical Meeting of the Combustion Institute
March 21, 2011
Presenting: Bryan Weber

## Slide 2: Introduction
Butanols – 4 Isomers
Motivation – Why Butanol?
  n-Butanol is a second generation biofuel with the potential to replace ethanol and gasoline
  The isomers of butanol have potential as high-octane gasoline additives
  The butanol system is the smallest alcohol system with primary, secondary and tertiary alcohol groups

## Slide 3: Previous Work
Since 2010, there have been nearly 30 butanol combustion studies
A number of these studies have been applications based, covering such devices as diesel engines, SI engines, and turbines
Although fundamental work has also expanded, there are still only limited data available for many conditions, especially high pressure/low temperature

## Slide 4: Previous Work
Black et al.1 have measured ignition delays of n-butanol in a shock tube at low pressure and high temperature (< 8 bar, 1100-1800 K)
Moss et al.2 have measured ignition delays of all four isomers of butanol in a shock tube at low pressure and high temperature (< 4 bar, 1200-1800 K)
Grana et al.3 have measured flame speeds of the isomers of butanol
Hansen et al.4 have studied three low pressure premixed flames of n-butanol and identified isomer-resolved intermediate species
Heufer et al.5, Vranckx et al.6, and Stranic et al.7 have investigated high pressure ignition delays of n-butanol in a shock tube (up to 90 bar, 795-1200 K)
1. Black, G., Curran, H., Pichon, S., Simmie, J. M., and Zhukov, V., Combustion and Flame, Vol. 157, No. 2, 2010, pp. 363-373.
2. Moss, J. T., Berkowitz, A. M., Oehlschlaeger, M. A., Biet, J., Warth, V., Glaude, P., and Battin-Leclerc, F., The Journal of Physical Chemistry. A, Vol. 112, No. 43, 2008, pp. 10843-10855.
3. Grana, R., Frassoldati, A., Faravelli, T., Niemann, U., Ranzi, E., Seiser, R., Cattolica, R., and Seshadri, K., Combustion and Flame, Vol. 157, 2010, pp. 2137-2154.
4. Hansen, N., Harper, M.R., and Green, W.H., 7th US National Combustion Meeting, Georgia Institute of Technology, Atlanta, GA, March 20-23, 2011, paper 1B09
5. Heufer, K.A., Fernandes, R. X., Olivier, H., Beeckmann, J., and Peters, N., Proceedings of the Combustion Institute, Vol. 33, 2011, pp.359-366.
6. Vranckx, S., Heufer, K.A., Lee, C., Olivier, H., Schill, L., Kopp, W.A., Leonhard, K., Taatjes, C.A., Fernandes, R.X., Combustion and Flame, 2011, Article in Press, doi:10.1016/j.combustflame.2010.12.028
7. Stranic, I., Chase, D., Harmon, J., Yang, S., Davidson, D.F., and Hanson, R.K., 7th US National Combustion Meeting, Georgia Institute of Technology, Atlanta, GA, March 20-23, 2011, paper 1B11

## Slide 5: Objectives
Provide complementary data to the previous studies using a Rapid Compression Machine
  Focus on high pressure and low to intermediate temperature conditions
Provide validation studies for the existing reaction mechanisms
  Cover many pressure ranges, equivalence ratios, and fuel loading conditions
Experimental conditions for all four isomers:
  PC= 15 bar, TC= 725-820 K, ϕ= 1.0, O2/N2 air

## Slide 6: Rapid Compression Machine (1)
Obtain experimental data for autoignition delays at elevated pressures and low-to-intermediate temperatures, using a heated rapid compression machine

## Slide 7: Rapid Compression Machine (2)
Single, retractable piston
Piston is pneumatically driven and hydraulically stopped, with compression time around 30 ms
Piston is machined with crevices to contain roll-up vortex created by piston motion

## Slide 8: Rapid Compression Machine (3)
Pressure and Temperature from Top Dead Center (TDC) are reported as “compressed conditions”, PC and TC
Ability to vary PC and TC independently
  PC up to 45 bar
  TC between 660-1100 K
Fuel and oxidizer are preheated and mixed in a 15 L mixing tank to ensure homogeneity

## Slide 9: Definition of Ignition Delay
Ignition criteria is the maximum rate of pressure rise
Ignition delay is the time difference from the end of compression to ignition point
Each condition is repeated at least 6 times to ensure repeatability

## Slide 10: Experimental Results (1)
No two-stage ignition or NTC region for any of the fuels under these conditions
sec-, tert- and iso-butanol do not deviate significantly from the non-reactive pressure trace

## Slide 11: Experimental Results (2)
Non-reactive case replaces oxygen with nitrogen to eliminate oxidation reactions but maintain the specific heat ratio
Pressure traces for n-butanol deviate from non-reactive case
Indicates minor pre-ignition heat release

## Slide 12: Experimental Results (3)
n-Butanol is more reactive than iso-butanol and sec-butanol, which are more reactive than tert-butanol
As the temperature goes down, iso-butanol and sec-butanol appear to become less reactive than tert-butanol

## Slide 13: Experimental Comparisons
Comparison of the data for n-butanol from this work and the work by Heufer et al.5, Vranckx et al.6, and Stranic et al.7
More complete sets in the neighborhood of 800 K are necessary to “connect the dots”
8. Weber, B.W., Kumar, K., Zhang, Y., and Sung, C.J., Combustion and Flame, 2011, Article in Press doi:10.1016/j.combustflame.2011.02.005

## Slide 14: Types of Simulations
Simulations of ignition delay are performed in CHEMKIN-PRO9 using four mechanisms available in the literature
Constant Volume, Adiabatic simulations have initial conditions set to the pressure and temperature conditions at TDC, and neglect heat loss to the reactor walls
Variable Volume simulations have the reactor volume as a controlled function of time
  Used to compute TC by matching the experimental pressure trace during compression
  Include effects of heat loss after compression by including parameters deduced from non-reactive experimental cases
9. CHEMKIN-PRO, Software Package, Ver. 15092, Reaction Design, San Diego, CA, 2008.

## Slide 15: Variable Volume Simulations
Most of the reaction mechanisms do not have ignition near the experimental value despite matching the compression stroke quite well
This is due to the fact that these do not include low temperature chemistry of butanol, the lack of which causes over-prediction of the ignition delay in this temperature range

## Slide 16: Simulations of n-Butanol
Simulations for n-butanol with a newer mechanism (Hansen et al.4) agree the best of any tested mechanism
Crossover point of constant volume, adiabatic simulations and variable volume simulations determined by balance of heat loss and chemical reactivity

## Slide 17: Simulations of n-Butanol
Agreement with ϕ = 0.5 in air is reasonable and variable volume simulations improve the slope of the simulations
Agreement with ϕ = 2.0 experiments is somewhat worse, especially for variable volume cases

## Slide 18: Simulations of Isomer Autoignition
Most mechanisms over predict the ignition delay of all the isomers, but the mechanisms by Moss et al.2 and Grana et al.3 do not include low temperature chemistry
The mechanism by Hansen et al.4 generally performs relatively better
Variable Volume simulations improve results for n- and iso-butanol

## Slide 19: Simulations of Isomer Autoignition
Experiments
Simulations

## Slide 20: Summary
New autoignition delay data has been collected for all four isomers of butanol at elevated pressure and low to intermediate temperature conditions
One (very recent) reaction mechanism predicts the ignition delay reasonably well for n-, tert- and iso-butanol, but gives somewhat poorer results for sec-butanol
Future work will expand the pressure, temperature, and equivalence ratio range of the experiments

## Slide 21: Acknowledgements
This work was supported as part of the Combustion Energy Frontier Research Center, an Energy Frontier Research Center funded by the U.S. Department of Energy, Office of Science, Office of Basic Energy Sciences, under Award Number DE-SC0001198.
We thank Dr. K. Kumar at the University of Connecticut for his help